## Slide 1: SECCHI Operations During the Extended Mission
Simon Plunkett
SECCHI Operations Lead
STEREO SWG
Pasadena, CA
February 3, 2009

## Slide 2: Current SSR1 Synoptic Program
Telescope | # Images and Size (pixels) | Exposure (seconds) | Cadence (minutes) | Total Images/Day | Compression Scheme | Total Mbits/Day
EUVI | 1 2k x 2k (171) 1 2k x 2k (171) 1 2k x 2k (195) 1 2k x 2k (195) 1 2k x 2k (284) 1 2k x 2k (304) 1 2k x 2k (304) 4 2k x 2k (All) | 4 16 16 16 32 4 4 16/16/32/4 | 2.5 120 10 120 10 10 120 1440 | 575 11 133 11 143 133 11 4 | ICER6 ICER4 ICER5 ICER4 ICER6 ICER5 ICER4 ICER0 | 
COR1 | 3 1k x 1k (pB) | 1.7 | 10 | 432 | ICER5 | 
COR2 | 3 2k x 2k (pB) 1 2k x 2k (B) 1 2k x 2k (B) | 6 6 72 | 30 30 1440 | 142 48 1 | ICER3 ICER3 HC4 | 
HI1 | 1 1k x 1k | 1200 | 40 | 36 | Rice | 
HI2 | 1 1k x 1k | 4950 | 120 | 12 | Rice | 
Total |  |  |  | 1693 |  | 4870.4

## Slide 3: Current SSR2 Synoptic Program
Telescope | # Images and Size (pixels) | Exposure (seconds) | Cadence (minutes) | Total Images/Day | Compression Scheme | Total Mbits/Day
EUVI | 1 2k x 2k (171) 1 2k x 2k (171) 1 2k x 2k (195) 1 2k x 2k (284) 1 2k x 2k (304) | 4 16 16 32 4 | 2.5 5 10 5 2.5 | 525 274 142 167 429 | ICER6 ICER4 ICER4 ICER6 ICER4 | 907.7 944.5 489.5 288.7 1478.8
COR1 | 3 1k  1k | 1.7 | 10 | 432 | ICER5 | 1103.3
EUVI SSR2 observations are interleaved with SSR1 observations to increase the image cadence in all wavelengths by at least a factor of 2 from that obtained with SSR1 alone.
COR1 SSR2 observations are interleaved with SSR1 observations for an effective image cadence of 5 minutes.
COR2 and HI images are onboard sums of individual images with shorter exposures.
Program fills SSR2 in about 3.7 hours, after which the oldest data get overwritten, unless an event trigger is set.
This program takes a total of 6275 images per day (SSR1 and SSR2 combined).
  Some of these images are also processed for space weather.
Notes: Laid out in planning tool 8/18/05 (using H-compress).

## Slide 4: Science Objectives During Extended Mission
Origin of SEPs
CME Initiation
CME propagation
3D reconstruction
  Triangulation using coronagraphs?
Campaign observations (e.g. L4/L5 campaigns)
SSR1 observations continue to provide the background synoptic program, with reduced image cadence and/or spatial resolution compared to nominal mission.
Increased reliance on SSR2 (event buffer) observations to meet science objectives.

## Slide 5: Data Volume During Extended Mission
Date Ahead | Date Behind | Telemetry Rate (kbps) | Pass Duration (hours) | SECCHI Data Volume (Mbits)*
Jan 2007 | Jan 2007 | 720 | 4 | 6158
Oct 2008 | Sep 2008 | 480 | 5 | 5048
May 2009 | Jun 2009 | 360 | 6 | 4475
Aug 2009 | Sep 2009 | 240 | 7 | 3371
May 2010 | Dec 2009 | 160 | 8 | 2433
Apr 2011 | Nov 2010 | 120 | 8 | 1716
Sep 2011 | Sep 2011 | 96 | 8 | 1286
Aug 2012 | Aug 2012 | 30 | 10 | 167
* Based on known variables and current experience.

## Slide 6: Proposed SSR1 Synoptic Program
Telescope | # Images and Size (pixels) | Exposure (seconds) | Cadence (minutes) | Total Images/Day | Compression Scheme | Total Mbits/Day
EUVI | 1 2k x 2k (171) 1 2k x 2k (171) 1 2k x 2k (195) 1 2k x 2k (284) 1 2k x 2k (304) | 4 16 16 32 4 | 5 120 120 120 120 | 288 12 12 12 12 | ICER6 ICER4 ICER4 ICER6 ICER4 | 
COR1 | 3 512 x 512 (pB) 1 512 x 512 (B) | 1.7 1.7 | 240 5 | 18 282 | ICER7 ICER7 | 
COR2 | 3 1k x 1k (pB) 1 1k x 1k (B) | 6 6 | 240 15 | 18 90 | ICER6 ICER6 | 
HI1 | 1 1k x 1k | 1200 | 60 | 24 | Rice | 
HI2 | 1 1k x 1k | 4950 | 120 | 12 | Rice | 
Total |  |  |  | 780 |  | 1680.0
  EUVI emphasis is on one wavelength at any time.
COR emphasis is on total B, with reduced spatial resolution (but increased cadence for COR1).
Minimal impact on HI observations (HI1 cadence reduced from 40 minutes to 60 minutes).
Fits within the expected SECCHI daily data volume at 120 kbps.