## Slide 1
STEREO Project
Ron Denissen – APL Project Manager
Dan Wilson– APL Mission System Engineer

## Slide 2
Project
Scientist
J. Gurman
Mission Director
D. Quinn
Mission System Engineer
Josephine San
FDF
Project
Manager
R. A. Denissen
Mission
Operations
D. Ossing
System
Engineering
D. Wilson
DSN
Technical
SSC
W. Thompson
Science
Teams
DSN
Scheduling
Payload
Operations
Teams
GSFC
APL
JPL
NRL, UCBerkeley, UNH, UMinn
Mission
Operation
Team
Subsystem
Lead
Engineers
STEREO Phase E Organization Chart

## Slide 3: Program Status
Operations
  Began automated unattended tracks April 30,2007
  Operations team is 6 full time staff. Total manpower is approximately 11 MM/M
  Downlink rates: Varies, 720 to 160 Kbps depends on antenna size and track elevation
  Switched MOC to CCSDS SLE telemetry standard in July 2011
  Began using ESA stations (35 meter) in January 2012
    Due to very high DSN loading
    Approved through December 2012
  Mission operations center still collecting 4 – 5 Gbits per day in support of the science mission.
Special Observatory Events
  Spacecraft are 230 degrees apart
  >110 instrument calibration events and roll events
  30 High Gain Antenna Calibrations (every 6 months)
  84 Momentum Dumps (~every 6 weeks on both spacecraft)

## Slide 4
DSN Interface Changes
2011
Jan - DSN Service Scheduling Software Implementation
May - SLE TLM Implementation
Jun - 160 kbps Rate Change – AHEAD (both S/C, 8 hr tracks)
Jul - 160 kbps Rate Change – BEHIND
2012
Nov - 120 kbps Rate Change – BEHIND
2013
May - 120 kbps Rate Change – AHEAD

## Slide 5: Issues and Concerns
ST anomalies on both spacecraft.
  Last occurrence, April 10, 2011, on AHEAD
Increasing track lengths cause more data gaps.
Aging spacecraft and ground system
  Wheel noise
  Blanket deterioration
  Ground system replacements
APL current contract expires in September of 2012. Two options exist
  1 year proposal to align with science authorization from Senior advisory Board
  2 year proposal as we have been doing.