## Slide 1: Spacecraft and Ground Segments Status
March 21, 2014
Dan Ossing
STEREO Mission Operations Manager
(240) 228-8319

## Slide 2: STEREO Phase E Organization Chart
Project
Scientist
J. Gurman
Mission Director
D. Quinn
Mission System Engineer
Josephine San
FDF
Project
Manager
R. A. Denissen
Mission
Operations
D. Ossing
System
Engineering
D. Wilson
DSN
Technical
SSC
W. Thompson
Science
Teams
DSN
Scheduling
Payload
Operations
Teams
GSFC
APL
JPL
NRL, UCBerkeley, UNH, UMinn
Mission
Operation
Team
Subsystem
Lead
Engineers

## Slide 3: Program Status
Operations
  Began automated unattended tracks April 30,2007
  Operations team is 6 full time staff. Total manpower is approximately 11 MM/M
  Downlink rates: Varies, 720 to 120 Kbps depends on antenna size and track elevation
  Switched MOC to CCSDS SLE telemetry standard in July 2011
  Began using ESA stations (35 meter) in January 2012
    Due to very high DSN loading
    Awaiting new NASA/ESA agreement
  Mission operations center still collecting 3 – 5 Gbits per day in support of the science mission.
Special Observatory Events
  36 instrument roll events to observe Comet ISON
  37 High Gain Antenna Calibrations (every 6 months)
  125 Momentum Dumps (~every 6 weeks on both spacecraft)
  >127 instrument calibration and roll events

## Slide 4: Spacecraft Status
Both observatories operating nominally using reduced gyro operations
IMU status (gyros)
  AHEAD
    IMU-A – failed in April 2007
    IMU-B – limited remaining life
  BEHIND
    IMU-A – limited remaining life
    IMU-B – failed in January 2014
  Reduced gyro operations uses IMU only when high rate data is required, i.e., momentum dumps, instrument rolls, etc.
Reaction Wheel Stiction
  AHEAD – Wheel 1
  BEHIND – Wheels 3 & 4

## Slide 5: Ground Segment Status
All MOC peripheral equipment, i.e., PCs, network equipment, UPS batteries, projectors, monitors, printers, and RAID arrays refreshed in 2012.
Refresh of Solaris Unix systems in progress
  Switching to Intel based Sun Unix systems

## Slide 6: Concerns
Superior Solar Conjunction in 2015
  Untested configuration
MOC Unix system refresh